## Slide 1: Demo
Accessing Raspberry Pi 5

## Slide 2: Setup
Wifi router
Rpi-5
Switch

## Slide 3: A first time run
A first time run might need a User Interface (UI)
Using an HDMI with a keyboard and a mouse.
VNCTiger is used instead of directly using HDMi.

## Slide 4: A first time run: Using VNC
Insert the RPi-5 IP address then ’connect’.
Insert your credentials

## Slide 5: A practical Deployment scenario
Take the scenario where many devices are connected to a switch and you need to access them.
  A solution is to connect to them using ‘SSH’

## Slide 6: A practical Deployment scenario How to use ssh
Open the terminal
Find the device IP:
  Use ifconfig
Ping (i.e., send packets) to the device to confirm connectivity.
  ping -c 5 <IP>
If succeeded, connect using ssh:
  ssh <user_name>@<IP>

## Slide 7: A practical Deployment scenario Use the device via ssh
pwd to check you current directory
ls to check the content
cd to navigate through the directories
Example:
  cd Documents/MoI
  mkdir live_demo
  cd live_demo
  nano hello_demo.py
    Create and edit a new file named ‘hello_demo.py’
  Write a hello world python script, exit and save.
  Run the script using python hello_demo.py