## Slide 1: Lab 5: Arithmetic and Number Representations
ECE265P Hardware For Machine Learning

## Slide 2: Floating-Point Number
Example: 32-bit floating-point number in IEEE 754
Sign 8 bit Exponent
23 bit Fraction (significant / mantissa)
(-1)sign × (1 + Fraction) × 2Exponent-127
Exponent Bias = 127 = 28-1-1
How to represent 0.265625?
0.265625 = 1.0625 × 2-2 = (1 + 0.0625) × 2125-127
0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
125
0.0625
23 22 21 20 2-1 2-2 2-3 2-4

## Slide 3: Floating-Point Number Example: 32-bit floating-point number in IEEE 754
Sign 8 bit Exponent
23 bit Fraction
(-1)sign × (1 + Fraction) × 2Exponent-127
Normal Numbers, Exponent≠0
- | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | -
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
+∞ (positive infinity)
-∞ (negative infinity)
NaN (Not a Number)
(-1)sign × Fraction × 21-127
Subnormal Numbers, Exponent=0
much waste. revisit in fp8.

## Slide 4: Floating-Point Number Example: 32-bit floating-point number in IEEE 754
Sign 8 bit Exponent
23 bit Fraction
Exponent | Fraction=0 | Fraction≠0 | Equation
00H = 0 | ±0 | subnormal | (-1)sign × Fraction × 21-127
01H … FEH = 1 … 254 | normal |  | (-1)sign × (1 + Fraction) × 2Exponent-127
FFH = 255 | ±INF | NaN | 
±0 2-149 (1-2-23) 2-126
subnormal values
…
2-126
normal values
(1+1-2-23)×2127

## Slide 5: Numeric Data Types
Sign 5 bit Exponent 10 bit Fraction
Sign: -
Exponent: 100012 - 1510 = 1710 - 1510 = 210
Fraction: 11000000002 = 0.7510
Decimal Answer = - (1 + 0.75) × 22 = -1.75 × 22 = -7.010
•
•
•
•
1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Question: What is the following IEEE half precision (IEEE FP16) number in decimal?
Exponent Bias = 1510

## Slide 6: Numeric Data Types
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Question: What is the decimal 2.5 in Brain Float (BF16)?
2.510 = 1.2510 × 21
•
•
•
•
Sign: +
Exponent Binary: 110 + 12710 = 12810 = 100000002
Fraction Binary: 0.2510 = 01000002 Binary Answer
Exponent Bias = 12710
Sign
8 bit Exponent
7 bit Fraction

## Slide 7: Numeric Data Types (Microscaling)
An MX-compliant format is characterized by three components:
• Scale (𝑋) data type / encoding
• Private elements (𝑃𝑖) data type / encoding
• Scaling block size (𝑘)
The bit widths are represented by the following symbols:
• w: number of bits used to encode the shared scale 𝑋
• d: number of bits used to represent each element 𝑃𝑖
Notes: All 𝑘 elements (𝑃𝑖) have the same data type and, therefore, the same bit-width. The scale factor
𝑋 is shared across all k elements. The data types of the elements and scale are chosen
independently. In this sense, MX can be seen as a mechanism to build a vector data type from
scalar data types.
The bit widths are represented by the following symbols:
• w: number of bits used to encode the shared scale 𝑋
• d: number of bits used to represent each element 𝑃𝑖

## Slide 8: Microscaling
Notes: All 𝑘 elements (𝑃𝑖) have the same data type and, therefore, the same bit-width. The scale factor
𝑋 is shared across all k elements. The data types of the elements and scale are chosen
independently. In this sense, MX can be seen as a mechanism to build a vector data type from
scalar data types.
The bit widths are represented by the following symbols:
• w: number of bits used to encode the shared scale 𝑋
• d: number of bits used to represent each element 𝑃𝑖

## Slide 9: Microscaling
Element Data Types
- 𝑆, 𝐸, and 𝑀 are the values of the Sign, Exponent, and Mantissa fields, respectively.
- 𝑏𝑖𝑎𝑠 is the exponent bias.
- 𝑚 is the number of mantissa bits
MX_FP
MX_INT
Notes: All 𝑘 elements (𝑃𝑖) have the same data type and, therefore, the same bit-width. The scale factor
𝑋 is shared across all k elements. The data types of the elements and scale are chosen
independently. In this sense, MX can be seen as a mechanism to build a vector data type from
scalar data types.
The bit widths are represented by the following symbols:
• w: number of bits used to encode the shared scale 𝑋
• d: number of bits used to represent each element 𝑃𝑖

## Slide 10
FP6 Encoding
Microscaling
Notes: All 𝑘 elements (𝑃𝑖) have the same data type and, therefore, the same bit-width. The scale factor
𝑋 is shared across all k elements. The data types of the elements and scale are chosen
independently. In this sense, MX can be seen as a mechanism to build a vector data type from
scalar data types.
The bit widths are represented by the following symbols:
• w: number of bits used to encode the shared scale 𝑋
• d: number of bits used to represent each element 𝑃𝑖

## Slide 11: Microscaling
Notes: All 𝑘 elements (𝑃𝑖) have the same data type and, therefore, the same bit-width. The scale factor
𝑋 is shared across all k elements. The data types of the elements and scale are chosen
independently. In this sense, MX can be seen as a mechanism to build a vector data type from
scalar data types.
The bit widths are represented by the following symbols:
• w: number of bits used to encode the shared scale 𝑋
• d: number of bits used to represent each element 𝑃𝑖

## Slide 12: Microscaling
V = [4.2, -3.1]
shared_exp = log24-2=0
emaxelem
step 1:
Notes: shared_exp contains an offset of emax_elem to map the max input exponent to the largest binade in the element data format

## Slide 13: Microscaling
X=2^0=1
emaxelem
step 2:
Notes: shared_exp contains an offset of emax_elem to map the max input exponent to the largest binade in the element data format

## Slide 14: Microscaling
step 3:
bias=2^(2-1)-1=1
V = [4.2/1, -3.1/1]= [4.2, -3.1]
Element Data Types
step 4: FP6_E2M3: 4.2
4.2=(-1)^0 * 2^(E-1) * (1 + 2-3 * M) = 22 * ( 1 + 2-3 * 0.4)
S=0
E=3 -> 11
M_real = 0.4 → M_int = 0 → 000
4.2 -> 0 11 000 -3.1 -> 1 10 100
Notes: shared_exp contains an offset of emax_elem to map the max input exponent to the largest binade in the element data format

## Slide 15: Microscaling
step 5: Encoding scale for storing
X=1 E8M0
bias = 28-1-1=127
1 = 2E-127 * (1+20 * M) -> E=127, M=0
X->01111111
Notes: shared_exp contains an offset of emax_elem to map the max input exponent to the largest binade in the element data format

## Slide 16: Numeric Data Types (Microscaling)
V = [4.2, -3.1]
01111111
0 11 000
1 10 100
Sign
Exponent
Fraction

## Slide 17: Microscaling
4.2 -> 0 11 000
-3.1 -> 1 10 100
23-1 * (1 + 2-3 * 0)=4
-1 * 22-1 * (1+2-3*4)= -3
After Quantizaiton
Before Quantizaiton
Notes: shared_exp contains an offset of emax_elem to map the max input exponent to the largest binade in the element data format